Wi-Fi firmware for ESP32

Rafael Conceição, nº 41486, e-mail: A41486@alunos.isel.pt, tel.: 967568496
Eduardo Tavares, nº 49454, e-mail: A49454@alunos.isel.pt, tel.: 912400426

Advisors:
Diego Passos, e-mail: diego.passos@isel.pt
Fernanda Passos, e-mail: fernanda.passos@isel.pt

March 2025

Introduction

There has been an increase in the density of wireless networks caused by the increase of mobile devices, sensors, and actuators. Due to these there is a necessity to be able to test new technics and protocols for such environments, which can be quite costly.
This project will try to address this by creating a low cost platform to allow developers to experiment in high density wireless areas. The hardware used in this project is fairly limited, not being able to match any standard already defined on IEEE 802.11, due to frequency and modulation of the signals required. Despite such limitations, our project’s implementation will still serve as a base for the spirit of wi-fi, which can be used to test the efficacy of various related technics, with variations on the error rate an throughput derived from the hardware limitations mentioned before.

Tools

For this project we will use Arduino IDE as the development environment, an ESP32 board, and a C1101 as a radio. We will use the library provided by the advisors which will provide the drivers for the radio.
The programming language used for this project will be C and C++.

Requirements

Mandatory:
- Implementation of IEEE 802.11 CSMA/CA
- Implementation of IEEE 802.11 RTS/CTS
- Implementation of IEEE 802.11 NAV
- Implementation of IEEE 802.11 backoff exponential
- Implementation of RSSI
- Implementation of a traffic generation module
Optional:
An application that allows for more fined tuned configuration of the nodes.

Milestones

- 10/3 – Deliver the project proposal
- 28/4 – Progress report
- 2/6 – Beta delivery with preliminary report
- 12/7 – Final delivery with final report, and presentation

References
[1] "Tecnologias de Redes Sem Fio". RNP/ESR, 2016 (available at: https://www.scribd.com/document/388714941/Tecnologias-de-redes-sem-fio-pdf)

[2]