Wi-Fi firmware for ESP32

Rafael Conceição, nº 41486, e-mail: A41486@alunos.isel.pt , tel.: 967568496
Eduardo Tavares, nº 49454, e-mail: A49454@alunos.isel.pt , tel.: 912400426

Advisors:
Diego Passos, e-mail: diego.passos@isel.pt
Fernanda Passos, e-mail: fernanda.passos@isel.pt

March 2025

Introduction

There has been an increase in the density of wireless networks caused by the increase of mobile devices, sensors, and actuators. Due to these there is a necessity to be able to test new techniques and protocols for such environments, which can be quite costly.
This project will try to address this by creating a low cost platform to allow developers to experiment in high density wireless areas, using cheap low wattage MCUs. The hardware used in this project is fairly limited, not being able to match any standard already defined on IEEE 802.11 [1] [2], due to frequency and modulation of the signals required. Despite such limitations, our project’s implementation will still serve as a base for the spirit of Wi-Fi, which can be used to test the efficacy of various related techniques, with variations on the error rate and throughput derived from the hardware limitations mentioned before.
By the end of this project, we expect to have made simultaneous communication possible between multiple nodes of our network.

Analysis

Implementing wireless communication, a basic need is to address collision to avoid interference between different nodes transmitting data at the same time. To achieve this, we plan to implement the CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance), with RTS/CTS. This protocol requires every participant to check if the channel is being used/reserved, and to announce its turn, along with the estimated time it will need it.
However, the process above necessitates that every node has their clocks synchronized. On real hardware, each clock will have different rhythm. Various methods exist, but all of them ultimately have to be done periodically to fix any offset caused with time. For this project’s completion, we intend to use the PTP (Precision time protocol) as defined in IEEE 1588.

Tools

For this project we will use Arduino IDE as the development environment, an ESP32 board, and a C1101 as a radio. We will use the library provided by the advisors which will provide the drivers for the radio.
The programming language used for this project will be C and C++.

Requirements

Mandatory:
- Implementation of IEEE 802.11 CSMA/CA
- Implementation of IEEE 802.11 RTS/CTS
- Implementation of IEEE 802.11 NAV
- Implementation of IEEE 802.11 backoff exponential
- Implementation of RSSI
- Implementation of a traffic generation module
Optional:
An application that allows for more fined tuned configuration of the nodes.

Milestones

- 10/3 – Deliver the project proposal
- 28/4 – Progress report
- 2/6 – Beta delivery with preliminary report
- 12/7 – Final delivery with final report, and presentation

References

[1] "Tecnologias de Redes Sem Fio". RNP/ESR, 2016 (available at: https://www.scribd.com/document/388714941/Tecnologias-de-redes-sem-fio-pdf)

[2] Computer Networking: A Top Down Approach, by James F. Kurose and Keith W. Ross, 7th Edition